## Slide 1: Title presentation
Name speaker | Place

## Slide 2: Index
Chapter
Chapter
Chapter
  Slide name
  Slide name
Chapter
Chapter
Chapter

## Slide 3: Implementation Details
      Capturing Images from the Network Camera
The system starts by capturing real-time scene images through the network camera. This step initiates the entire image processing workflow, providing continuous visual data from the environment.
The network camera is connected to the Raspberry Pi or any processing unit. Libraries such as OpenCV are used to initialize the camera device and set its parameters (e.g., resolution, frame rate) to capture images.Pellentesque habitant morbi.
Converting RGB Images to HSV Color Space
The captured images are usually represented in the RGB (Red, Green, Blue) color space. This step converts the RGB color space images into the HSV (Hue, Saturation, Value) color space.
The HSV color space is more suitable for color-related tasks because it separates color and brightness information, making color detection less affected by changes in lighting conditions.
Notes: 1. 从网络摄像头捕捉图像
过程：系统首先通过网络摄像头实时捕捉场景图像。这一步是整个图像处理流程的起点，摄像头持续提供环境中的视觉数据。
技术细节：网络摄像头连接到 Raspberry Pi 或任何处理单元。使用特定的库（如OpenCV）来初始化摄像头设备，并设置相应参数（如分辨率、帧率）以捕获图像。
2. 将RGB图像转换为HSV色彩空间
过程：捕获的图像通常以RGB（红、绿、蓝）色彩空间表示。这一步将RGB色彩空间的图像转换为HSV（色调、饱和度、亮度）色彩空间。
技术细节：HSV色彩空间更适合处理与颜色有关的任务，因为它将颜色和亮度信息分离开来，使得颜色检测不那么受光照变化的影响。

## Slide 4: Thresholding and Morphological Operations
      Thresholding:
By setting specific HSV range values, objects of a particular color (e.g., a ball) are identified, and the image is converted into a binary image (containing only black and white), where white represents the target objects and black represents the background.
OpenCV library is utilized for thresholding to remove irrelevant colors from the image, leaving only parts that match the color of the ball.
      Morphological Operations:
      Erosion: Removes the edges of white areas, helping to remove small white noise and also separate two touching objects.
      Dilation: Increases the size of white areas to compensate for parts removed in the erosion step, restoring the shape of the object.
      Technical Details: Erosion and dilation operations are often used in sequence to purify the image. OpenCV provides erode and dilate functions for these operations.
Notes: 3. 进行阈值处理、形态学操作（侵蚀和扩张）
阈值处理：
  过程：通过设置特定的HSV范围值来识别特定颜色的物体（如球），并将图像转换为二值图像（仅包含黑白两色），其中白色代表目标物体，黑色代表背景。
  技术细节：利用OpenCV库进行阈值处理，可以移除图像中的不相关颜色，仅保留与球颜色匹配的部分。
形态学操作：
  侵蚀：去除白色区域的边缘部分，有助于移除小的白色噪声，也可以分离两个接触的物体。
  扩张：增大白色区域，用于弥补侵蚀步骤中去除的部分，恢复物体的形状。
  技术细节：侵蚀和扩张操作通常连续使用来净化图像，OpenCV提供了erode和dilate函数进行这些操作。

## Slide 5: Precisely Locate the Ball
      Drawing Contours:
      Process: Finds and draws contours in the binary image, where contours can be viewed as continuous points that form the boundary of an object.
      Technical Details: OpenCV’s ‘findContours’ function is used to find contours in the image. This step is crucial for identifying and locating spherical objects.
      Drawing Circles:
      Process: Using contour information to find the smallest enclosing circle, approximating the detected ball's position and size.
      Technical Details: The ‘minEnclosingCircle’ function in OpenCV calculates the smallest circle that encloses a given set of points (contour points), simplifying the task of locating the ball.
Notes: 绘制轮廓和圆圈以精确定位球
绘制轮廓：
过程：在二值图像中查找并绘制轮廓，其中轮廓可以被视为形成对象边界的连续点。
技术细节：OpenCV 的“findContours”函数用于查找图像中的轮廓。 此步骤对于识别和定位球形物体至关重要。
画圆圈：
过程：利用轮廓信息找到最小外接圆，近似检测到的球的位置和大小。
技术细节：OpenCV 中的“minEnendingCircle”函数计算包围给定点集（轮廓点）的最小圆，从而简化了定位球的任务。

## Slide 6: Control and Movement
Raspberry Pi as Brain: The Raspberry Pi serves as the central processing unit, handling image data analysis and making decisions based on predefined algorithms. It sends commands to the motors based on the processed information.
Four-Wheel Drive System: The SunFounder PiCar-4WD's four-wheel drive system allows for precise control over speed and direction. This ensures the car can swiftly adjust its path to follow the ball, enhancing its ability to maneuver around obstacles and across various surfaces.
Motor Control: The vehicle uses DC motors for movement, with speed and direction controlled by the Raspberry Pi. The integration of motor driver modules enables the Raspberry Pi to manage the motors efficiently, allowing for smooth acceleration and turning.
Servo-Controlled Steering: The PiCar-4WD includes servo motors for steering control, offering the ability to make sharp or subtle changes in direction. This is crucial for accurately tracking and following the ball during experiments.
Real-Time Tracking: Combining the Raspberry Pi's processing power with the PiCar-4WD's responsive movement capabilities allows for real-time tracking of objects. The system can dynamically adjust its actions based on the position and movement of the ball, ensuring continuous engagement.
Software-Hardware Integration: The success of the PiCar-4WD in following and interacting with the ball lies in the seamless integration of software algorithms with the vehicle's hardware components. This synergy between the Raspberry Pi's decision-making and the car's physical movements enables effective real-time response to visual cues.
Notes: Raspberry Pi 作为大脑：Raspberry Pi 作为中央处理单元，处理图像数据分析并根据预定义的算法做出决策。它根据处理后的信息向电机发送命令。
四轮驱动系统：SunFounder PiCar-4WD 的四轮驱动系统可以精确控制速度和方向。这确保了汽车可以快速调整其路径以跟随球，从而增强其绕过障碍物和跨越各种表面的能力。
电机控制：车辆使用直流电机进行运动，速度和方向由 Raspberry Pi 控制。电机驱动模块的集成使 Raspberry Pi 能够有效管理电机，从而实现平稳的加速和转向。
伺服控制转向：PiCar-4WD 包括用于转向控制的伺服电机，能够对方向进行急剧或细微的改变。这对于实验期间准确跟踪和跟随球至关重要。
实时跟踪：将 Raspberry Pi 的处理能力与 PiCar-4WD 的响应运动功能相结合，可以实时跟踪物体。该系统可以根据球的位置和运动动态调整其动作，确保持续的攻击。
软硬件集成：PiCar-4WD 在跟随球和与球交互方面的成功在于软件算法与车辆硬件组件的无缝集成。Raspberry Pi 的决策与汽车的物理运动之间的协同作用可以实现对视觉提示的有效实时响应。

## Slide 7: Testing and Evaluation
      Object Capture Distance Test:
      Determines the system's maximum detectable distance for balls, verifying the system's effectiveness at various distances.
      Color Recognition Capability Test:
      Tests the system's ability to recognize balls of different colors by changing the ball's color.
      Light Intensity Impact Test:
      Evaluates the system's performance under various lighting conditions, ensuring stable operation in diverse environments.
      Speed Test:
      Measures the speed at which the robot tracks and approaches the ball, demonstrating the system's response speed and execution efficiency.
Notes: 测试与评估
物体捕捉距离测试：测定系统能够识别的最远球体距离，验证了系统在不同距离下的有效性。
颜色识别能力测试：通过更换不同颜色的球，测试系统对各种颜色球的识别能力。
光照强度影响测试：评估系统在不同光照条件下的性能，确保系统在多种环境下稳定工作。
速度测试：测量机器人追踪并接近球的速度，证明了系统的反应速度与执行效率。

## Slide 8: Division of Labor
      Jiayi Wu
      Image processing with OpenCV
      Pu Li
      Image processing with OpenCV
      Suju Li
      Control and Movement
      Ruhao Han
      Control and Movement
      Shan Jiang
      Testing and Evaluation

## Slide 9: Text dominant, image 25%
      Lorem ipsum dolor sit amet
    Consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies.
Nunc viverra imperdiet enim.
Fusce est.
Vivamus a tellus.
  Pellentesque habitant morbi.
  Proin pharetra nonummy pede.
  Mauris et orci.

## Slide 10: Text and image egual, 50%-50%
      Lorem ipsum dolor sit amet
    Consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies.
Nunc viverra imperdiet enim.
Fusce est.
Vivamus a tellus.
  Pellentesque habitant morbi.
  Proin pharetra nonummy pede.
  Mauris et orci.

## Slide 11: Image dominant, text 25%
      Lorem ipsum dolor sit amet
Nunc viverra imperdiet enim.
Fusce est.
Vivamus a tellus.
  Pellentesque habitant morbi.
  Proin pharetra nonummy pede.
  Mauris et orci.

## Slide 12: Only image

## Slide 13: Text and 4 images
      Lorem ipsum dolor sit amet
    Consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies.
Nunc viverra imperdiet enim.
Fusce est.
Vivamus a tellus.
  Pellentesque habitant morbi.
  Proin pharetra nonummy pede.
  Mauris et orci.

## Slide 14: Text and 2 images
      Lorem ipsum dolor sit amet
    Consectetuer adipiscing elit. Maecenas porttitor congue massa. Fusce posuere, magna sed pulvinar ultricies.
Nunc viverra imperdiet enim.
Fusce est.
Vivamus a tellus.
  Pellentesque habitant morbi.
  Proin pharetra nonummy pede.
  Mauris et orci.

## Slide 15: Graph
Chart: 
| Category 1 | Category 2 | Category 3 | Category 4
Subject 1 | 2 | 3 | 1 | 4
Subject 2 | 4 | 2 | 1 | 3
Subject 3 | 3 | 1 | 4 | 2
Subject 4 | 4 | 3 | 2 | 1

## Slide 16: Video

## Slide 17: Title closure